| Datalogger Comparison Table | Inputs/Outputs Memory Current Drain Temperature Range Dimensions Please note: Due to fundamental differences in operating system capabilities and compatibility, the specifications of the CR200-series dataloggers/wireless sensors are published separately. |
| --- | --- |

| Inputs/Outputs | CR510 | CR10X | CR23X | CR5000 | CR7 | CR9000 |
| --- | --- | --- | --- | --- | --- | --- |
| Differential Analog Channels (a) | 2 | 6 | 12 | 20 | 14 per 723 Card or 723T Card | 14 per CR9050 Module or CR9055 Module |
| Maximum Input Voltage (b) | ±2500 mV | ±2500 mV | ±5000 mV | ±5000 mV | ±5000 mV (726 Card) ±50 V (723 Card) | ±5000 mV (CR9050 Module) ±50 V (CR9055 Module) |
| Analog Voltage Resolution | to 0.33 µV | to 0.33 µV | to 0.33 µV | to 0.33 µV | to 50 nV | to 0.76 µV |
| A/D Bits | 13 | 13 | 15 | 16 | 16 | 16 |
| Input Impedance | 20 Gohm | 20 Gohm | 20 Gohm | 20 Gohm | 2.5 Gohm | 2.5 Gohm |
| Input Bias Current | ±9 nA | ±9 nA | ±10 nA max | ±10 nA max | ±100 pA | ±3 nA typ. |
| Scan Rate (c) | 64 Hz | 64 Hz | 100 Hz | 1667 Hz | 80 Hz | 4,500 Hz |
| Burst Mode | n/a | 750 Hz | 1500 Hz | n/a | n/a | 100,000 Hz |
| Pulse Channels (d,e) | 2 | 2 | 4 | 2 | 4 per 724 Card | 12 per CR9071 Module |
| Excitation Channels (e) | 2 switched voltage (f) | 3 switched voltage | 4 switched voltage | 4 switched voltage 4 switched current | 8 per 725 Card | 10 per CR9060 Module |
| Excitation Voltage (g) | ± 2500 mV | ± 2500 mV | ± 5000 mV | ± 5000 mV | ± 5000 mV | ± 5000 mV |
| CAO Channels (e,h) | 0 | 0 | 2 | 2 | 2 per 725 Card | 6 per CR9060 Module |
| Digital Ports (e,i) | 1 output | 8 I/O | 8 I/O | 8 I/O | 8 output per 725 Card | 8 output per CR9060 Module 16 output per CR9071 Module |
| Voltage Requirements | 9.6 to 16 Vdc | 9.6 to 16 Vdc | 11 to 16 Vdc | 11 to 16 Vdc | 9.6 to 15 Vdc | 9.6 to 15 Vdc |
| Memory | CR510 | CR10X | CR23X | CR5000 | CR7 | CR9000 |
| Program Memory (Bytes) | 16K active 16K auxillary | 16K active 16K auxillary | 16K active 16K auxillary | 2M | 1.8K | 256K Flash |
| Data Storage (data points) | 62,280 | 62,280 | 1 million | Table Format | 18,396 | Table Format |
| Optional Data Memory (data points) | 1 million | 1 million | 2 million | expandable through PC cards | n/a | n/a |
| Current Drain | CR510 | CR10X | CR23X | CR5000 | CR7 | CR9000 |
| Quiescent | 1.3 mA typical | 1.3 mA typical | 2 mA display off | 1.5 mA sleep mode | 3.5 to 6.0 mA typical | n/a |
| Processing | 13 mA | 13 mA | 45 mA | 4.5 mA@1 Hz 200 mA@5 KHz | 16 mA | 750 to 1000 mA typ. |
| Measurement | 46 mA | 46 mA | 70 mA |  | 100 mA | 750 to 1000 mA typ. |
| Temperature Range | CR510 | CR10X | CR23X | CR5000 | CR7 | CR9000 |
| Standard (°C) | -25 to +50 | -25 to +50 | -25 to +50 | -25 to +50 | -25 to +50 | -25 to +50 |
| Extended (°C) | -55 to +85 | -55 to +85 | -40 to +80 | -40 to +85 | -40 to +70 | -40 to +70 |
| Dimensions | CR510 | CR10X | CR23X | CR5000 | CR7 | CR9000 |
| Size (inches) | 8.0 x 1.5 x 4.0 | 9.0 x 3.5 x 3.0 | 9.5 x 7.0 x 3.8 | 8.25 x 9.5 x 4.5 | 20 x 13 x 10 | 18 x 14 x 9 |
| Size (cm) | 21.3 x 3.8 x 9.9 | 22.9 x 8.9 x 7.4 | 24.1 x 17.8 x 9.6 | 21.0 x 24.1 x 11.4 | 50.8 x 33.0 x 25.4 | 45.7 x 34.3 x 22.9 |
| Weight | 1.0 lbs (0.4 kg) | 1.5 lbs (0.68 kg) | 8.3 lbs (3.8 kg) | 12.2 lbs (5.5 kg) | 40 lbs (18.2 kg) | 40 lbs (18.2 kg) |

(a) Each differential channel can be configured as 2 single-ended channels; expandable with multiplexers. 
(b) Precision 2:1 and 10:1 voltage dividers are available to extend these ranges. 
(c) One measurement with data transfer without interruption. 
(d) Switch closure, high frequency square wave, or low-level AC sine wave.
(e) Expansion peripherals are available, see SDM literature.
(f) Port C2/P3 is input only and can be software configured as an SDI-12 port, a binary input, or as a switch closure counter (40 Hz maximum). 
(g) All excitation and CAO (Continuous Analog Output) channels can be individually programmed as outputs by the end-user. 
(h) CAO channels can be programmed to hold a constant value or vary with the magnitude of a measurement. 
(i) 0 V low, 5 V high; the CR510, CR10X, and CR23X have ports that are configurable for interrupt subroutines.

MJ Technologies,Inc.    “Total Customer Satisfaction”